## Slide 1
Automated Vehicles
By: Kristen Bake

## Slide 2: History: Five Eras
1950-2000: Safety/Convenience Features
Cruise Control
Seat Belts
Antilock Brakes
2000-2010: Advanced Safety Features
Electronic Stability Control
Blind Spot Detection
Forward Collision Warning
Lane Departure Warning
2010-2016: Advanced Driver Assistance Features
Rearview Video Systems
Automatic Emergency Braking
Pedestrian Automatic Emergency Braking
Rear Cross Traffic Alter
Lane Centering Assist
2016-2025:
Partially Automated Features
Lane Keep Assist
Adaptive Crise Control
Traffic Jam Assist
2025+:
Fully Automated Safety Features

## Slide 3: Levels of Automation

## Slide 4: Benefits
Safety
Removing the driver or assisting the driver in the chain of events that can result in a crash will help to protect drivers and passengers, bicyclists, and pedestrians
Mobility
Could increase mobility for seniors, people with disabilities, and expand transportation options for underrepresented communities
Economic/Societal
Motor vehicle crashes cost billions each year- minimizing the number of crashes through automation could reduce this cost.
Environmental
Automated ride share could transform land use, and increased efficiency could reduce air pollutants
Efficiency/Convenience
Time spent in traffic delays increase fuel costs and vehicle transmissions- automated systems could reduce this time and increase efficiency and convenience

## Slide 5: The Tech

## Slide 6: Sensors for Perception
Artificial Vision
  Provides information such as spatial (shape, size, distance), dynamic (motion), and semantic (shape analysis)
  Popular across domains for decades; low cost
Radar
  High frequency electromagnetic waves measure distance to objects
  Independent of light and weather conditions
LiDAR
  Calculates distance with laser light pulse
  Highly accurate distance measurements
  Capable of creating accurate 3D digital maps

## Slide 7
Differing Capabilities
Artificial Vision
  Highly dependent on environmental visibility
Radar
  Differing reflectivity of various materials may result in false positives and false negatives
LiDAR
  Difficulty detecting small objects (such as bars and wires)
  Colored objects that absorb most radiation may be invisible (e.g., black cars)
  Dependent on weather conditions
Safety in Redundancy
Adequacy for relevant types of information
Robustness under atmospheric/environmental factors

## Slide 8: Challenges of Partial Automation

## Slide 9: Driver Safety and Intervention
Effects of Automation Use…
  Inattention
  Trust
  Fatigue
  Complexity
  Skill Atrophy
  Complacency
May Impact …
  Takeover Readiness
  “Automation Surprises”
  Out-of-the-Loop

## Slide 10: Interface Design
Relative freedom in iterative design and testing phases may allow for greater exploration and development of possible design solution
Controls and Displays
Transparency
Simplify
Prevention of Premature Engagement
Maintain Driver:
Skill
Wakefulness
Attentiveness

## Slide 11: Public Acceptance
Overall Positive:
  Most popular with young men in urban environments
  Generally positive with older people (65+) as means of continued mobility
Concerns:
Software Hacking
Data Sharing and Misuse
Safety
Legal
Perceived Loss of Control and Enjoyment
Impacted by:
Media Coverage
Familiarity
Cost/WTP
Risk vs. Benefit
Similarity in driving styles

## Slide 12: Implications

## Slide 13: The Ripple Model (Milakis, van Arem, van Wee)
Used to conceptualize the sequential effects of the adoption on automated driving on several aspects of society
Not necessarily unidirectional

## Slide 14: First-Order Implications
Travel Cost
  Cost may reduce with time and widespread adoption
  Time cost reduced
  Value of time not perceived to increase
Road Capacity
  Higher penetration rate will bring greater benefits
  40% penetration rate threshold for significant benefits
Travel Choices
  Increase in travel demand due to changes in destination choice, mode choice, and mobility
  Shared Avs further Increase miles traveled

## Slide 15: Second-Order Implications
Vehicle Ownership
  Shared Avs could replace from 67% to over 90% of vehicles of equal mobility
  Vary by penetration rate and presence or absence of public transportation
Land Use
  Could trigger further urban expansion
  Land used for parking shifted to peripheral zones
Transport Infrastructure
  Shared Avs reduce parking space requirements over 90%
  Vary on mode, penetration rate, and existing public transport

## Slide 16
Third-Order Implications
Fuel Efficiency
  Higher levels of automation and penetration rate could lead to higher fuel savings
Long-Term Energy Consumption and Air Pollution
  Net effect uncertain
    More efficient travel, but longer travel distance and increased travel by underserved populations
Emissions
  Lower emissions, particularly in higher levels of automation, penetrations, and shared use
Economy
  Jobs in transportation and logistics sector have high probability of becoming automated within 20 years
Public Health
  Gap in the research!
Safety
  Level 3+ may enhance traffic safety
  Behavioral adaptation, software vulnerabilities may compromise traffic safety benefits
  Full automation may not deliver high levels of benefits until high penetration rates are achieved
Social Equity
  Increased safety and mobility for elderly
  Up to 14% increase in travel demand
  Possibility of social justice incorporation

## Slide 17: Future Directions

## Slide 18: Future Research and Focus
Long-Term Impact on Emissions, Pollution, Public Health, etc.
Methodology of Testing
Mapping Strategies
Sharing and Collaboration among Researchers
Factors Effecting or Impeding Acceptance
Solving Existing Challenges First

## Slide 19: Thank You!

## Slide 20: Sources