## Slide 1
Introduction to Probabilistic Risk Assessment
Jisuk Kim
Jisuk.kim@inl.gov

## Slide 2: Contents
\
01 What is PRA?
02 Why do we perform PRA?
03 How to perform PRA?

## Slide 3: 01 02 03
What is PRA?
Probabilistic Risk Assessment
[Probabilistic Safety Assessment, Reliability and Safety Engineering]
  The chance of injury or loss resulting from exposure to a source of danger
    Likelihood of occurrence of the given adverse event
    Magnitude(or severity) of the adverse event
  Risk = Likelihood X Magnitude(or Severity)

## Slide 4: 01 02 03
What is PRA?
Probabilistic Risk Assessment
Deterministic
to demonstrate that a facility is tolerant to identified faults/hazards that are within the “design basis”, thereby defining the limits of safe operation.
Probabilistic
to provide a realistic estimate of the risk presented by the facility. All potential credible accidents are included.
[https://risktec.tuv.com/risktec-knowledge-bank/qualitative-deterministic-risk-assessment/deterministic-or-probabilistic-analysis/]
[Mustaffa, Z.B., Gelder, P.V., & Vrijling, H. (2009). A Discussion of Deterministic Vs. Probabilistic Method In Assessing Marine Pipeline Corrosions.]

## Slide 5: 01 02 03
Why do we perform PRA?
[https://www.nrc.gov/reading-rm/doc-collections/fact-sheets/3mile-isle.html]
1) Secondary cooling system failed
Auxiliary
Feedwater
2) Auxiliary feedwater pump also did
not work
X
[WASH-1400 The Reactor Safety Study, USNRC]
3) The relief valve on the top of PZR open
Pressurizer
Relief valve
Safety Injection
6) Operator cannot identify the
malfunction, and stop the safety
injection
X
4) The valve did not reset into a closed
position
Pressure ↑
5) Instrumentation did not alert the
state of the valve
X
TMI accident(1979)
A small LOCA resulting from a combination of human factors and mechanical failure.

## Slide 6: 01 02 03
Why do we perform PRA?
WASH-1400
[WASH-1400 The Reactor Safety Study, USNRC]
In small LOCA,
The Coolant is lost at a lower rate than in Large LOCA.
The reactor vessel still maintains high pressures in small LOCA.
Operators have to deal with small-break LOCAs by using high pressure, low-volume pumps to cover and cool the reactor core.
→ Importance of Small break LOCA, compared to Large break
LOCA.
→ WASH1400 did prove prescient concerning the TMI accident
outcome.
Large break LOCA vs. Small break LOCA
(LOCA: Loss of coolant accident)

## Slide 7: 01 02 03
Why do we perform PRA?
Safety Goal
Qualitative
Safety Goal
Quantitative Safety Goals
Surrogate Goals
Quantitative Safety Goals
  The risk of prompt and cancer fatalities in the area near a nuclear power plant should not exceed 0.1% of the sum of prompt and cancer fatalities.
Surrogate Goals (Performance Goals)
  CDF < , LERF <
  Future NPPs : 1/10 of existing NPPs
← The results of PRA
“How safe is safe enough?”

## Slide 8: 01 02 03
Why do we perform PRA?
PRA can answer
    What could go wrong? (Accident scenarios)
    How likely is it? (Frequency, Probability)
    What would the consequences be?

## Slide 9: 01 02 03
How to perform PRA?
Level 2 PSA
Containment failure frequency(CFF)
/ Large Early Release Frequency(LERF)
Core damage frequency
(CDF)
Level 1 PSA
Level 3 PSA
Offsite consequence analysis(Fatality)
What would
the consequences be?
What could go wrong?
How likely is it?

## Slide 10: 01 02 03
How to perform PRA?
Level 1 PSA procedure
② Event tree A graphical depiction of a sequence of events
① Initiating event
Circumstances that put a plant in an off-normal condition
⑥ Quantification
Frequency, Probability
③ Fault tree
③ Fault tree
A graphical depiction of how a system can fail
④ Data
Failure rate of plant equipment from operating experience
⑤ Human Reliability Analysis
Analysis and quantification of human interactions and failure

## Slide 11: 01 02 03
How to perform PRA?
Example
Event tree
Fault tree
Success
Failure
Cause
Consequences
Top event
Basic events
Consequence
Causes

## Slide 12: 01 02 03
How to perform PRA?
Example
SGTR
(Steam Generator Tube Rupture)
Residual
Heat removal
Stop SI
Cooldown
ok
Reactor
trip
Reactor
trip
Control
Auxiliary
Feedwater
Control
Auxiliary
Feedwater
Safety
Injection
(SI)
Injection of SI
Isolation
faulted SG
Isolation
Core damage
ok
Fail
↓
↑
success
Human
Actions
01
Human
Actions
02
Human
Actions
03
Human
Actions
04
Human
Actions
#
. . .
. . .

## Slide 13: 01 02 03
Summary
Systematic tool for analyzing complex systems with information integration
  To determine the risk profile assessing weakness of a system.
Insights to improve human performance
  improve the human-machine interface
  Increase chances of recovery
  Improve procedures
Design flaws and cost-effective ways to eliminate them in design prior to construction and operation
Fault Tree Analysis
PRA
Initiating
Event
Analysis
Event
Tree
Analysis
Quantification
Human
Reliability
Analysis
Reliability Data Analysis
Accident scenarios, Frequency/Probability, Consequence

## Slide 14
Thank you for your attention